## Slide 1
’60’s TECHNOLOGY & ITS IMPACT ON RAAF

## Slide 2: RAAF of SIXTIES
A busy, busy Air Force ( Malaya, Ubon; 2, 9 & 35 SQNS in Vietnam)
24,000 people with in-house 3 level maintenance capability
thirteen new aircraft types introduced in decade (C130, Bloodhound, Mirage, Caribou, Iroquois, Viscount, Macchi, HS748 VIP, BAC111, Mystere, HS748 Nav, C130E, P3)

## Slide 3: READY OR NOT
  technical workforce proficiency standards raised with apprentice trade schools & tertiary quals for Eng O’s
  But many Eng & Maint processes mired in WW2 thinking
  Unforeseen left field ‘gotcha’s’
  Insight gained from bograt junior engineer’s experiences as the sole materials EngO in HQSC ‘65/’69

## Slide 4: New A/C brought Technology infusion
A/B & turboprop engines
Supersonic airframes
Systems architecture – increasing complexity (components/ black boxes)
Innovation in airframe design philosophy (‘safe life’ to ‘fail safe’)
C130A (58/59 intro) led the way into the 60’s

## Slide 6: Key C130 Enablers
T56 turboshaft powerplant (4,000+ HP for drag, wing lift, airspeed, altitude, pressurization, range needs, power/weight ratio).
effective wing – 133’ span, 10:1 aspect ratio, unique wing box monocoque, damage tolerant/fail safe structure,
Allowed internal ‘wet’ wing fuel storage

## Slide 7: C130 Wing Design Enablers
Fundamentally, aluminium alloy developments 1930’s/1950’s
Resulted in Al alloys with tensile strengths equiv to steel
  2024 (copper) - C130A/E’s, P3B (limited corrosion resistance)
  7075 (zinc) – C130H, P3C, gave 10% strength increase over 2024 with better corrosion resistance – used in Zero main spar!!

## Slide 10: SERIOUS C130A WING CORROSION
Flight line discovery early 60’s
Caused by excreta of a microbe (cladisporium resinae) living in wing tanks with water contamination
Large scale 2AD repair program (defuels, outer wings off, planks, spar caps replaced, polysulphide tank sealant repair)
Impacted capability levels
Intro of RAAF wide fuel quality control measures (above ground fuel farms, rigid daily fuel testing base/sqn, FSII additive)
OHS issues

## Slide 11: SUPERB DSTO SUPPORT
ARL for metallic material support of Al alloys, corrosion control, NDI
ARL provided on base practical NDI services for several years
DSL were great in organic material support ( ie fuels, microbes,sealants)
One has to compliment DSTO for their responsiveness
THEY WERE READY, WILLING & ABLE

## Slide 12: C130 CORROSION EXPERIENCE LED TO CRUCIAL RAAF TECHNICAL CAPABILITIES
Non-Destructive testing (eddy current, ultrasonic, dye penetrant) – in late 60’s, NDI kept Sabre, Canberra, Iroquois in air
Corrosion (intergranular, stress, filiform)
Fracture mechanics expertise
Composite repair expertise (C130 plank riser band aids)
All became crucial over next 3 decades (F111 particularly)

## Slide 13: AIRCRAFT SYSTEM COMPLEXITY
C130A & Mirage brought systems with componentry that generally needed ILM repair (specialized skills, centralized ATE)
RAAF had no component lifing, configuration management systems nor a base level component tracking system
Threatened to disrupt capability due spares shortages
Paper-based component handling system introduced until replaced by CAMM
EE77 maintenance recording system replaced by EE500

## Slide 14: TECH PUB SYSTEM
System of 1950’s totally outdated
  Couldn’t handle FSD of complex aircraft
  Depended on outmoded WW2 general pubs, AP’s, AEIGs, RMIG’s, ‘T’ Orders etc
  Replaced by 7000 AAP system (eg -1 FM, -2 MM, -3 IPB, -4 SS with specialized pub series for each aircraft type

## Slide 15: FURTHER TECHNICAL PROCESS IMPROVEMENTS
Configuration management (CMP’s, TMP’s)
Maintenance engineering assessment to validate maintenance requirements (the what/when)
Specialised maintenance facilities (laminar flow clean rooms, calibration labs)

## Slide 16: LOGISTICS IMPACT
Profusion of new aircraft brought large increase in RAAF stores inventory
Timely introduction of FSN classification system (US/NATO)
Somewhat intractable clash technical world working with part number authority to fit & stock managers

## Slide 17: Fast Fwd To 1980’s
Era of
  ageing A/C (C130, Caribou, Macchi, Iroquois, P3, F111)
  Digitised system architecture
  Airworthiness in jeopardy (accidents)

## Slide 18
Accidents & Airworthiness in jeopardy
Eg Macchi, Nomad, 707

## Slide 19: Ageing Aircraft
Intense disposal & life extension effort (LOTEX)
pressure to extend lives
Reliance on NDI expertise & SBI
Technology v convention
‘Woods & trees’

## Slide 20: AIRWORTHINESS IN JEOPARDY
Aircraft Losses (Macchi, Nomad, B707)
Updated RAAF engineering & airworthiness management systems required
Hence Blueprint 2020 & Airworthiness reviews leading to mandated engineering authorities & airworthiness boards

## Slide 21: SUMMARY
RAAF DID FAIR JOB OF ADAPTING TO ‘60’S TECHNOLOGY & IN GENERAL APPLIES INHERENT PLATFORM TECHNOLOGY WELL
BUT LESSONS LEARNT
  BE PREPARED FOR LEFT FIELD
  BE WARY OF IGNORING/MODIFYING CONVENTION
  VALUE OF SOVREIGN RESEARCH CAPABILITY
  OPPORTUNITIES FOR SKILL/PROCESS DEVELOPMENT

## Slide 22: Big picture issues - technology
Paucity of national research re technology despite clear examples of successful national technological developments
Lack of expert body to analyse technology needs
Leads to ad hoc introduction of technology largely through re-equipment projects

## Slide 23: FUTURE
Crystal ball:
  Adequacy of design/certification regulation & compliance v technology (eg 737 Max)
  Quality of build, performance etc (eg 787 composites, engine)
  Impact of AI on design, production standards